## Slide 1: DEE 4544 DIGITAL ELECTRONICS Chapter 1: Binary System and Logic Circuits
By : Dr. Noraisyah Tajudin
Email: noraisyahtajudin@lincoln.edu.my
Faculty of Engineering
Lincoln University College (LUC)
LECTURE 1
DATE : MARCH 2024

## Slide 2: Why binary number?
Binary is a language written with a combination of ones (1) and zeros (0) that computers use to carry out commands, inputs, or functions. Whatever you write onto a computer, a machine inside processes the input and converts it into binary.
  Each unit of memory media (hard disk, tape, CD …) has two states to represent 0 and 1
  Such physical (electronic) device is easier to make, less prone to error
    E.g., a voltage value between 0-3mv is 0, a value between 3-6 is 1 …

## Slide 3: The Advantage of Binary Number Systems
1. Binary devices are Simple and easy to build
An on/off switch is simple and easy to build. An on/off switch moves two pieces of metal together or moves them apart.
The same is true for the tiny devices inside of a silicon chip. On/off switches are relatively easy to fabricate.
2. Binary signals are Unambiguous (which gives them noise immunity)
It is easy to look at a digital signal that is only supposed to be on or off and decide which it is supposed to be.

## Slide 4
3. Flawless copies can be made of binary data
4. Anything that can be represented with some sort of pattern can be represented with a binary pattern

## Slide 5: Data Representation in Computer
In modern computers, all information is represented using binary values.
Each storage location (cell): has two states
  low-voltage signal => 0
  High-voltage signal => 1
  i.e., it can store a binary digit, i.e., bit
Eight bits grouped together to form a byte
Several bytes grouped together to form a word
  Word length of a computer, e.g., 32 bits computer, 64 bits computer

## Slide 6: Bytes and Bits
In binary, we have bytes and bits which are major components in writing binary.
Bit: a single 0 or 1 in a binary number
Byte: eight bits put together

## Slide 7: What is a gate?
The building blocks used to create digital circuits are logic gates
Combination of transistors that performs binary logic
There are three elementary logic gates and a range of other simple gates
Each gate has its own logic symbol which allows complex functions to be represented by a logic diagram
The function of each gate can be represented by a truth table or using Boolean notation

## Slide 8: LOGIC GATES
Types of gates
  NOT
  AND
  OR
  NAND
  NOR
  EX-OR
  EX-NOR
  BUFFER GATE

## Slide 9: NOT Gate
A NOT gate accepts one input value and produces one output value
By definition, if the input value for a NOT gate is 0, the output value is 1, and if the input value is 1, the output is 0
A NOT gate is sometimes referred to as an inverter because it inverts the input value

## Slide 10: AND Gate
An AND gate accepts two input signals
If the two input values for an AND gate are both 1, the output is 1; otherwise, the output is 0

## Slide 11: OR Gate
If the two input values are both 0, the output value is 0; otherwise, the output is 1

## Slide 12: NAND and NOR Gates
The NAND and NOR gates are essentially the opposite of the AND and OR gates, respectively.
They are also called universal gates.

## Slide 13: XOR Gate
XOR, or exclusive OR, gate
  An XOR gate produces 0 if its two inputs are the same, and a 1 otherwise

## Slide 14: XNOR Gate
The exclusive-nor gate or xnor is logically equivalent to
an xor gate followed by an inverter

## Slide 15
Logic Family Terminology
A digital logic family is a group of compatible devices with the same logic levels and supply voltages.
According to components used in the same logic family, digital logic families are classified as:
  Resistor-Transistor logic
  Diode- transistor logic
  Transistor-transistor logic
  MOS families----NMOS logic, PMOS logic, CMOS logic
  Emitter-Coupled Logic

## Slide 16
Characteristics of Digital Logic Families
Propagation delay
Power dissipation
Current and voltage parameter
Noise margin and logic voltages levels
Fan-in and Fan-out
Current Sinking
Current Sourcing
Speed Power Product

## Slide 17
Resistor – Transistor Logic (RTL)

## Slide 18: Resistor Transistor logic
It has a fan-out of 5.
Propagation delay is 25ns.
Power dissipation is 12mw.
Noise margin for low signal input is 0.4v.
Poor noise immunity.
lLow speed.

## Slide 19: Diode Transistor Logic
It has fan-out of 8.
It has high noise immunity.
Power dissipation is 12mw.
Propagation constant is average 30ns.
Noise margin is about 0.7v.

## Slide 20: Emitter Coupled Logic
Propagation delay is very low (<1ns).
ECL is fastest logic family.
ECL circuit usually operate with -ive supplies (+ive terminal is connected to ground).

## Slide 21: Transistor Transistor Logic
TTl has greater speed than DTL.
Less noise immunity.
Power dissipation is 10nw.
It has fan-in of 6 and fan-out of 10.
Propagation time delay is 5-15nsec.

## Slide 22: CMOS
Dissipates low power, power dissipation is typically 10 nW per gate.
The propagation delays are usually around 25 nS to 50 nS.
Noise immunity approaches 50% or 45% of the full logic swing.

## Slide 23
Thank You.