## Slide 1: DEE 4544 DIGITAL ELECTRONICS Chapter 4: Flip Flops, Counters and Registers
By : Dr. Noraisyah Tajudin
Email: noraisyahtajudin@lincoln.edu.my
Faculty of Engineering
Lincoln University College (LUC)
LECTURE 4
DATE : APRIL 2024

## Slide 2: Course content outline.
To understand the flip – flops and its Applications.

## Slide 3: Introduction
A sequential circuit consists of a feedback path and employs some memory elements.
Combinational logic
Memory elements
Combinational outputs
Memory outputs
External inputs
Sequential circuit = Combinational logic + Memory Elements

## Slide 4: Introduction
There are two types of sequential circuits:
  synchronous: outputs change only at specific time
  asynchronous: outputs change at any time
Multivibrator: a class of sequential circuits. They can be:
  bistable (2 stable states)
  monostable or one-shot (1 stable state)
  astable (no stable state)
Bistable logic devices: latches and flip-flops.
Latches and flip-flops differ in the method used for changing their state.

## Slide 5: Sequential Circuits
Combinational
Circuit
Memory Elements
Inputs
Outputs
Asynchronous
Synchronous
Combinational
Circuit
Flip-flops
Inputs
Outputs
Clock

## Slide 6: Memory Elements
Memory element: a device which can remember value indefinitely or change value on command from its inputs.
Characteristic table:
command
Memory element
stored value
Q
Q(t): current state
Q(t+1) or Q+: next state

## Slide 7: Memory Elements
Memory element with clock. Flip-flops are memory elements that change state on clock signals.
Clock is usually a square wave.
command
Memory element
stored value
Q
clock
Positive edges
Negative edges
Positive pulses

## Slide 8: Memory Elements
Two types of triggering/activation:
  pulse-triggered
  edge-triggered
Pulse-triggered
  latches
  ON = 1, OFF = 0
Edge-triggered
  flip-flops
  positive edge-triggered (ON = from 0 to 1; OFF = other time)
  negative edge-triggered (ON = from 1 to 0; OFF = other time)

## Slide 9: S-R Latch
Complementary outputs: Q and Q'.
When Q is HIGH, the latch is in SET state.
When Q is LOW, the latch is in RESET state.
For active-HIGH input S-R latch (also known as NOR gate latch),
R=HIGH (and S=LOW) a RESET state
S=HIGH (and R=LOW) a SET state
both inputs LOW a no change
both inputs HIGH a Q and Q' both LOW (invalid)!

## Slide 10: Latches
SR Latch
S R Q0 | Q | Q’
0 0 0 |  | 
0
1
0
0
0 | 1
Q = Q0
Initial Value

## Slide 11: Latches
SR Latch
S R Q0 | Q | Q’
0 0 0 | 0 | 1
0 0 1 |  | 
1
0
0
0
1 | 0
Q = Q0
Q = Q0

## Slide 12: Latches
SR Latch
S R Q0 | Q | Q’
0 0 0 | 0 | 1
0 0 1 | 1 | 0
0 1 0 | 0 | 
0
1
1
0
 | 1
Q = 0
Q = Q0

## Slide 13: Latches
SR Latch
S R Q0 | Q | Q’
0 0 0 | 0 | 1
0 0 1 | 1 | 0
0 1 0 | 0 | 1
0 1 1 |  | 
1
0
1
0
0 | 1
Q = 0
Q = Q0
Q = 0

## Slide 14: Latches
SR Latch
S R Q0 | Q | Q’
0 0 0 | 0 | 1
0 0 1 | 1 | 0
0 1 0 | 0 | 1
0 1 1 | 0 | 1
1 0 0 |  | 
0
1
0
1
1 | 0
Q = 0
Q = Q0
Q = 1

## Slide 15: Latches
SR Latch
S R Q0 | Q | Q’
0 0 0 | 0 | 1
0 0 1 | 1 | 0
0 1 0 | 0 | 1
0 1 1 | 0 | 1
1 0 0 | 1 | 0
1 0 1 |  | 
1
0
0
1
1 | 0
Q = 0
Q = Q0
Q = 1
Q = 1

## Slide 16: Latches
SR Latch
S R Q0 | Q | Q’
0 0 0 | 0 | 1
0 0 1 | 1 | 0
0 1 0 | 0 | 1
0 1 1 | 0 | 1
1 0 0 | 1 | 0
1 0 1 | 1 | 0
1 1 0 |  | 
0
1
1
1
0 | 0
Q = 0
Q = Q0
Q = 1
Q = Q’
0

## Slide 17: Latches
SR Latch
S R Q0 | Q | Q’
0 0 0 | 0 | 1
0 0 1 | 1 | 0
0 1 0 | 0 | 1
0 1 1 | 0 | 1
1 0 0 | 1 | 0
1 0 1 | 1 | 0
1 1 0 | 0 | 0
1 1 1 |  | 
1
0
1
1
0 | 0
Q = 0
Q = Q0
Q = 1
Q = Q’
0
Q = Q’

## Slide 18: Latches
SR Latch
S R | Q
0 0 | Q0
0 1 | 0
1 0 | 1
1 1 | Q=Q’=0
No change
Reset
Set
Invalid
S R | Q
0 0 | Q=Q’=1
0 1 | 1
1 0 | 0
1 1 | Q0
Invalid
Set
Reset
No change

## Slide 19: Latches
SR Latch
S R | Q
0 0 | Q0
0 1 | 0
1 0 | 1
1 1 | Q=Q’=0
No change
Reset
Set
Invalid
S’ R’ | Q
0 0 | Q=Q’=1
0 1 | 1
1 0 | 0
1 1 | Q0
Invalid
Set
Reset
No change

## Slide 20: Controlled Latches
SR Latch with Control Input
C S R | Q
0 x x | Q0
1 0 0 | Q0
1 0 1 | 0
1 1 0 | 1
1 1 1 | Q=Q’
No change
No change
Reset
Set
Invalid

## Slide 21: Controlled Latches
D Latch (D = Data)
C D | Q
0 x | Q0
1 0 | 0
1 1 | 1
No change
Reset
Set
C
Timing Diagram
D
Q
t
Output may change

## Slide 22: Controlled Latches
D Latch (D = Data)
C D | Q
0 x | Q0
1 0 | 0
1 1 | 1
No change
Reset
Set
C
Timing Diagram
D
Q
Output may change

## Slide 23: Latch Circuits: Not Suitable
Latch circuits are not suitable in synchronous logic circuits.
When the enable signal is active, the excitation inputs are gated directly to the output Q. Thus, any change in the excitation input immediately causes a change in the latch output.
The problem is solved by using a special timing control signal called a clock to restrict the times at which the states of the memory elements may change.
This leads us to the edge-triggered memory elements called flip-flops.

## Slide 24: Flip-Flops
Controlled latches are level-triggered
Flip-Flops are edge-triggered
C
CLK
Positive Edge
CLK
Negative Edge

## Slide 25: Flip-Flops
Master-Slave D Flip-Flop
D Latch
(Master)
D
C
Q
D Latch
(Slave)
D
C
Q
Q
D
CLK
CLK
D
QMaster
QSlave
Looks like it is negative edge-triggered
Master
Slave

## Slide 26: Flip-Flops
Edge-Triggered D Flip-Flop
D
Q
Q
D
Q
Q
Positive Edge
Negative Edge

## Slide 27: Flip-Flops
JK Flip-Flop
J
Q
Q
K
D = JQ’ + K’Q

## Slide 28: Flip-Flops
T Flip-Flop
D = TQ’ + T’Q = T  Q
J
Q
Q
K
T
D
Q
Q
T
D = JQ’ + K’Q
T
Q
Q

## Slide 29: Flip-Flop Characteristic Tables
D
Q
Q
D | Q(t+1)
0 | 0
1 | 1
Reset
Set
J | K | Q(t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | Q’(t)
No change
Reset
Set
Toggle
J
Q
Q
K
T
Q
Q
T | Q(t+1)
0 | Q(t)
1 | Q’(t)
No change
Toggle

## Slide 30: Flip-Flop Characteristic Equations
D
Q
Q
D | Q(t+1)
0 | 0
1 | 1
Q(t+1) = D
J | K | Q(t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | Q’(t)
Q(t+1) = JQ’ + K’Q
J
Q
Q
K
T
Q
Q
T | Q(t+1)
0 | Q(t)
1 | Q’(t)
Q(t+1) = T  Q

## Slide 31: Flip-Flop Characteristic Equations
Analysis / Derivation
J
Q
Q
K
J | K | Q(t) | Q(t+1)
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
No change
Reset
Set
Toggle

## Slide 32: Flip-Flop Characteristic Equations
Analysis / Derivation
J
Q
Q
K
J | K | Q(t) | Q(t+1)
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
No change
Reset
Set
Toggle

## Slide 33: Flip-Flop Characteristic Equations
Analysis / Derivation
J
Q
Q
K
J | K | Q(t) | Q(t+1)
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 
1 | 1 | 1 | 
No change
Reset
Set
Toggle

## Slide 34: Flip-Flop Characteristic Equations
Analysis / Derivation
J
Q
Q
K
J | K | Q(t) | Q(t+1)
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0
No change
Reset
Set
Toggle

## Slide 35: Flip-Flop Characteristic Equations
Analysis / Derivation
J
Q
Q
K
J | K | Q(t) | Q(t+1)
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0
 |  |  |  | K | 
 |  | 0 | 1 | 0 | 0
J |  | 1 | 1 | 0 | 1
 |  |  | Q |  | 
Q(t+1) = JQ’ + K’Q

## Slide 36: Flip-Flops with Direct Inputs
Asynchronous Reset
D
Q
Q
R
Reset
R’ | D | CLK | Q(t+1)
0 | x | x | 0

## Slide 37: Flip-Flops with Direct Inputs
Asynchronous Reset
D
Q
Q
R
Reset
R’ | D | CLK | Q(t+1)
0 | x | x | 0
1 | 0 | ↑ | 0
1 | 1 | ↑ | 1

## Slide 38: Flip-Flops with Direct Inputs
Asynchronous Preset and Clear
PR’ | CLR’ | D | CLK | Q(t+1)
1 | 0 | x | x | 0
D
Q
Q
CLR
Reset
PR
Preset

## Slide 39: Flip-Flops with Direct Inputs
Asynchronous Preset and Clear
PR’ | CLR’ | D | CLK | Q(t+1)
1 | 0 | x | x | 0
0 | 1 | x | x | 1
D
Q
Q
CLR
Reset
PR
Preset

## Slide 40: Flip-Flops with Direct Inputs
Asynchronous Preset and Clear
PR’ | CLR’ | D | CLK | Q(t+1)
1 | 0 | x | x | 0
0 | 1 | x | x | 1
1 | 1 | 0 | ↑ | 0
1 | 1 | 1 | ↑ | 1
D
Q
Q
CLR
Reset
PR
Preset

## Slide 41
Applications of Flip-Flops:
These are the various types of flip-flops being used in digital electronic circuits and the applications of Flip-flops are as specified below.
Counters
Frequency Dividers
Shift Registers
Storage Registers
Bounce elimination switch
Data storage
Data transfer
Latch
Registers
Memory

## Slide 42
Thank You