## Slide 1: DEE 4544 DIGITAL ELECTRONICS Chapter 5: Introduction to State Machines.
By : Dr. Noraisyah Tajudin
Email: noraisyahtajudin@lincoln.edu.my
Faculty of Engineering
Lincoln University College (LUC)
LECTURE 5
DATE : APRIL 2024

## Slide 2: Course content outline.
To understand the State Machines and their need.
To understand the Basic Concepts in State Machine Analysis.

## Slide 3
Storage
elements
A combinational circuit and storage elements are interconnected to form a sequential circuit.
The information stored at any time defines the state of the circuit at that time.
The next state of the storage elements is a function of the inputs and the present state.
Synchronous sequential circuit can be defined from the knowledge of its signals at discrete instants.
Sequential Circuits

## Slide 4
Logic blocks are classified as:
  Combinational and
  Sequential
Does sequential logic contain both combinational logic and memory?
  Yes
  No

## Slide 5
Combinational and Sequential Logic
Combinational logic does not have memory
It generates output solely according to the input and does not care about history
Often, we need a different reaction on the same input depending on the current state
E.g.
  Current state is 7 and input is 1, the new state and output are 8
  Current state is 15 and input is 1, the new state and output are
  To make the new state depends on the previous state, we need memory

## Slide 6
Sequential Logic and FSM
Computers are made of sequential logic blocks
Truth tables are used to design combinational logic, but can’t be used to design sequential logic
Finite state machines (FSM) are used instead
FSM describes a sequential logic block in terms of:
  Set of states,
  State transition function (defined on current state and input), and
  Output function (defined on current state and input, or on current state only)

## Slide 7: Why State Machines?
Goal: provide simple abstractions of complex systems
All computer systems are state machines
  registers and memory are state
  changes are transitions between states
  a program defines the way in which initial states are transformed into final states
  a programming language determines a set of programs (and hence, a set of machines)
Primary challenge will be to represent these very complex machines with simpler (more abstract) machines that we can reason about

## Slide 8: State Machines Are Often Used
When it is possible to abstract away irrelevant details, leaving only a small number of states
When we want to examine every possibility using exhaustive checking
For communication protocols and complex distributed algorithms (e.g., cache coherency)

## Slide 9: Informally ...
A state machine captures the idea that a system progresses through a set of states by performing (or responding to) a set of actions.
Thus there are two key concepts
  States
  Actions
A state machine definition must say
  what the possible states are
  what initial states the machine may start in
  what the possible actions are
  how the state changes when actions occur

## Slide 10: A (Very) Simple State Machine
World's simplest state machine
States: {stop}
Actions: {}
Initial state: {stop}
stop

## Slide 11
Another Simple Example
States: {alarm}
Actions: {beep}
Initial state: {alarm}
alarm
beep

## Slide 12: Moore vs. Mealy Machines
Definitions
Moore Machine
Outputs are function
solely of the current
state
Outputs change
synchronously with
state changes
Mealy Machine
Outputs depend on
state AND inputs
Input change causes
an immediate (asynchronous)
output change
State
Register
Clock
State
Feedback
X
Inputs
Z
Outputs
Combinational
Logic for
Next State
(FF Inputs)
Comb.
Logic for
Outputs)
Mealy only; no connection for Moore

## Slide 13: Moore

## Slide 14
Moore machines are faster
Mealy machines are smaller
Any Moore machine can be turned into a Mealy machine (and vice versa)

## Slide 15
Instead of using algebraic equations for next state and outputs of sequential network, it is more convenient and useful to express the information in tabular form.
Transition Tables :
The Transition Table or State Transition Table or State Table is the tabular representation of the transition and output equations. This table consist of Present State, Next State, external inputs and output variables. If there are n state variables then 2n rows are present in state table.
State machine notations :
Input Variables : External input variables to sequential machine as inputs.

## Slide 16
Output Variables : All variables that exit from the sequential machine are output variables.
State : State of sequential machine is defined by the content of memory, when memory is realized by using FFs.
Present State : The status of all state variable i.e. content of FF for given instant of time t is called as present state.
Next State : The state of memory at t+1 is called as Next state.
State Diagram : State diagram is graphical representation of state variables represented by circle. The connection between two states represented by lives with arrows and also indicates the excitation input and related outputs.

## Slide 17
Sequential Circuit Analysis (cont.)
  Generate State Diagram
    Circles (nodes) represent current or present state values
    Lines (arcs) represent how state and output values change
      Given the current state and current inputs, the next state and output values are indicated by the associated arc
    State diagram can have different forms depending on the type of sequential circuit output.
Present
State
Value
Next
State
Value
Inputs/outputs

## Slide 18
Output Variables : All variables that exit from the sequential machine are output variables.
B
1
A
0
Q0
11/10
Q1
x0
11/01
State diagram of J-K FF
0X
Application Table of FF
PS | NS | FF input | 
Q | Q+ | J | K
0 | 0 | 0 | X
0 | 1 | 1 | X
1 | 0 | X | 1
1 | 1 | X | 0

## Slide 19
Application Table of FF
PS | NS | FF i/p | 
Q | Q+ | S | R
0 | 0 | 0 | X
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | X | 0
State diagram of SR FF
0
1
01
00
10
01
00
10

## Slide 20
Application Table of FF
PS | NS | FF i/p
Q | Q+ | D i/p
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
State diagram of D FF
0
1
0
1
0
1

## Slide 21
Application Table of FF
State diagram of T FF
0
1
0
1
1
0
PS | NS | FF i/p
Q | Q+ | T i/p
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 22
Analysis of Sequential Circuits
Example 2
FF input Equations:
DA=AX+BX
DB=A’X
A+=DA
B+=DB
Output:
Y=X’(A+B)

## Slide 23
Analysis of Sequential Circuits
State Table:

## Slide 24
Basic Design Approach
Sequential Circuit design: Reverse of analysis
State diagram State table next s.e.
FF input eq. Circuit Diagram
Six Step Process
  1. Understand the statement of the Specification
  2. Obtain an abstract specification of the SSC
  3. Generate State Table
  4. Perform state assignment
  5. Choose FF types to implement SSC state register
  6. Implement the SSC

## Slide 25
Sequential Circuit Design
Design a sequence detector for the string “1101”. The output must be ‘1’ when the input matches this string
x
w
clock
Sequence
detector

## Slide 26
Sequential Circuit Design
Mealy state machine (remember that in this state machine the output is dependent on input changes and states)
A
B
C
D
0/0
1/0
1/0
1/0
0/0
0/0
1/1
0/0
Assign binary values to each state. Example:
A = 00, B = 01, C = 11, D = 10

## Slide 27
Sequential Circuit Design
Make Table FROM present state & input TO next state & output, and FF inputs.
A
B
C
D

## Slide 28
Sequential Circuit Design
K-maps of the states & the outputs
I
Q1 Q0
J1
I
Q1 Q0
K1
I
Q1 Q0
J0 = I
I
Q1 Q0
K0 = I’
= IQ0
= Q0’
I
Q1 Q0
Output = IQ1Q0’

## Slide 29
Sequential Circuit Design
Layout Diagram
J1 = IQ0
K1 = Q0’
J0 = I
K0 = I’
Output = IQ1Q0’

## Slide 30
Moore State Machine for the sequence detector 110
Sequential Circuit Design
A
B
C
D
state
A
A/0
B/0
C/0
D/1
0
1
1
1
0
0
1
0

## Slide 31
Summary
Finite state machines form the basis of many digital systems
Designs often start from clear specifications
Develop state diagram and state table
Optimize using combinational design techniques
Mealy or Moore implementations possible
  Can model approach using HDL.

## Slide 32
Thank You